One of the biggest inconveniences of sending a message via fax 
is that the fax machine is usually located outside of one's own office 
environment.  This means obtaining a hardcopy of information to be 
sent, finding a fax machine from which to send it, getting to that 
machine, filling out forms and then finally sending out the message.  
If a fax machine could be included as part of the campus network at 
large, that string of intermediate steps would be eliminated for a lot 
of people.  
     CSO now offers as a test service an electronic mail to fax gateway.  
This gateway makes it possible for any UIUCnet user to send an e-
mail message to someone with access to a fax machine.  

How It Works
     An ordinary, simply formatted (ASCII) e-mail message is 
addressed to the CSO e-mail/fax gateway.  The gateway, with its 
special hardware and software configuration, converts the e-mail 
message into a format that can be sent over a telephone line to a 
receiving fax machine, where the message is reproduced on paper.  
     The e-mail messages that the gateway receives are placed in a 
temporary storage space, called a transmission "queue," where they 
wait in line until the designated time to be sent out.  Presently, faxes 
are sent out from the gateway every twenty minutes.  The 
originating user will be notified if the phone number doesn't fit 
within the specified guidelines.  It may take mere minutes or up to 
an hour for the fax to get out, depending on how busy the queue is, 
how long the message is, and whether the receiving fax machine 
accepts the fax.  The gateway will attempt to send out the fax six 
times before giving up.  Once the gateway either successfully 
transmits the message or gives up trying, such will be indicated 
through e-mail to the originating user.  During the test period, faxes 
may be sent anywhere in the U.S. free of charge.  
     This service is owned and operated by the Computing Services 
Office (CSO) which is part of the University of Illinois. It is intended 
for use by the faculty, staff and students in conjunction with their 
duties at the University. Restrictions on use are essentially the same 
as using a campus telephone.

INSTRUCTIONS FOR USE

The Address:
     In the "To:" or "Cc:" field of the e-mail message header, one uses 
an address of the form:
	namephone#@fax.uiuc.edu
where namephone# is the segment, or field, of the address that gives 
the name of the person for whom the fax is destined in addition to 
the receiving fax machine's telephone number.  There are certain 
restrictions on what this field should contain.  First of all, consider 
the "namephone#" field to be divided into two subsections.  The 
"name" subsection  is meant to contain details about the addressee, 
such as their proper name, room address, etc.  It may consist of 
characters A-Z, a-z, 0-9, -(dash), and _(underscore) but NO blank 
spaces or @ signs are allowed.   Also, the name subsection must not 
end with a digit.  The second subsection of the "namephone#" field is 
meant for the phone number of the fax, and directly follows the 
name subsection.  It may only contain numerical digits 0-9 without 
any punctuation marks  (i.e. no dashes or parentheses).  
     The entire "namephone#" field, incorporating both subsections, is 
currently limited to 40 characters in length.  Formation of an address 
should take into account the above-stated rules and follow the 
guidelines listed in Table 1.
     As an example,  an e-mail address to a fax machine might look 
something like: 
Michael_Gardner_173_DCL_40916@fax.uiuc.edu
     For users of IBM VM/CMS systems such as CSO's VMD, mail 
programs like Bitnote and Ricemail will readily accept long e-mail 
addresses as are necessary in using the e-mail/fax gateway service.  
However, procedure and instructions for AISS PROFS users have not 
yet been worked out and will be published at a later date.  

TABLE 1:

For calls to fax machines	Use this form
with numbers like:		of address:

1. On-campus calls*:
	2-xxxx		   name2xxxx@fax.uiuc.edu
	3-xxxx		   name3xxxx@fax.uiuc.edu
	4-xxxx       name4xxxx@fax.uiuc.edu

2. Local calls; the University prefix "9"is included automatically:

	xxx-xxxx  	   namexxxxxxx@fax.uiuc.edu     

3. Near local calls: theUniversity prefix "9" is included automatically:

	1-xxx-xxxx	   name1xxxxxxx@fax.uiuc.edu

4. Long distance calls: accepted with or without the "1" prefix; "9xx" 
area codes not allowed:

	xxx-xxx-xxxx       namexxxxxxxxxx@fax.uiuc.edu

			   or, alternatively,

	1-xxx-xxx-xxxx     name1xxxxxxxxxx@fax.uiuc.edu


   *Note that 333-xxxx & 244-xxxx won't work.   



The Message
     There are a limited number of options accessible through the test 
version of the e-mail/fax gateway.  E-mail messages in plain ASCII 
text format will be accepted.  ASCII form feed (ctrl-L or octal 014) 
will cause a page break.  Normal page size is 80 characters by 66 
lines.  If the gateway detects lines longer than that, it will switch to a 
132 characters by 88 line format, using a smaller font.   
     Six attempts to send the fax will be made, each about a minute 
apart, providing a twelve minute window.  If the receiving fax is 
busy all that time, the fax will fail.  An e-mail message will be sent to 
the originator of the message, informing him/her of success or failure 
of the gateway's attempt to send out the fax. 
			
Appearance of Resultant Message 
     The current e-mail to fax gateway always creates at least a two 
page fax. The first page is divided into three parts: logo, routing, and 
cover. The second page and beyond contains the actual e-mail 
message. The "logo" is a standard UIUCnet e-mail to fax graphic. The 
"routing" section contains text stating the "To:" address of the fax 
(derived from namexxxx@fax.uiuc.edu) and the source of the fax 
(the CSO e-mail to fax gateway). The "cover" section contains generic 
reply instructions and a portion of the sender's mail header.  

Return Correspondence
     Users who send faxes are strongly encouraged to include in the 
text of the message a complete return address including the sender's 
proper name, location, and telephone number.  Information about 
where to return fax correspondence should also be included.  Faxes 
presently cannot be returned to a user through the campus network 
primarily because of formatting conversion problems.  If a 
formatting standard is resolved, delivery of fax images over UIUCnet 
may be offered at some future time.
     Return faxes should be directed to one's closest fax machine.  
Many campus and departments have fax machines, and the 
University's Office of Telecommunications operates a fax for general 
use.  Return faxes may be indirectly sent to any University 
college/department by accessing the Telecommunications fax 
machine at telephone number 217-333-9758. Messages should 
include the addressee's name and campus address. The Office of 
Telecommunications will forward these transmissions through 
campus mail.  For more informations, contact the Customer Service 
Office at 333-5137. 
     
     At this time details have not been completely worked out for a 
general use University fax machine to which return faxes may be 
directed.  Until a such a fax is available, users are encouraged to 
make arrangements with a campus office or department.

     If you have any additional questions concerning this service you 
may address them to gardner@ux1.cso.uiuc.edu or Michael G. Gardner 
at 244-0914.