## Slide 1: Spinner Assembly: Design Review
Payload Mounting Plate
Flexible Coupling Attachment
Bearing Housing
Multi-Load Bearing
Hollow Shaft
65 Tooth Steel Gear 65mm PD
2500 Tick Encoder Disk
Insert
Spacers
Bus Cover Plate
Optical Encoder
Slip Ring Spacer
Encoder Mounting Bracket
Slip Ring
Not Shown:
-Micro DC Motor
-15 Tooth Brass Gear 15mm PD
-Small Gear Mounting Collar
-Flexible Coupling
Notes: Type notes here

## Slide 2: Spinner Assembly: Final Model
Specifications
  Max Angular Velocity: 1.7 Hz
  Motor Controller: Pololu QiK TTL Interface
  Slip Ring Channels: 12
  Dimensions (Interface Space): 100mm x 100mm x 18mm

## Slide 3: Spinner Assembly: Demonstration

## Slide 4: Spinner Assembly: Qualitative Testing
Spinner Assembly rotating at 1.7Hz
Oscilloscope
Signal Generator
-Sine Wave
-Square Wave
Setup:
Sample Square Wave Output (10 Volts/div, 1kHz):
Transmitted Signal
Input
Difference

## Slide 5: Spinner Assembly: Qualitative Testing
Results:
  Noticeable signal distortion appears at frequencies >1 KHz
  Significant signal distortion appears at signal frequencies >1 MHz
Conclusion:
  LL serial transmission rate: 70 KHz
  Problems due to signal distortion will be minimal
5 MHz Sine Wave
Input
Difference
Transmitted Signal

## Slide 6: Spinner Assembly: Quantitative Testing
Computer
Serial TX
Serial RX
Spinner Assembly rotating at 1.7 Hz
Setup:
Results:
  1,000,000 bytes sent; 0 errors
  Error probability <0.0000054 with 99% confidence
Conclusion:
  Slip ring interface is suitable for serial data transfer
Notes: Type notes here

## Slide 7: Spinner Assembly: Encoder Testing
Relative roll angle between the bus and payload is given by an optical encoder with 2 arc minute accuracy
US Digital Sample Timing Characteristics
Channel A
Channel B
Index
Observed Timing Characteristics
Index
Channel B
Channel A

## Slide 8: Spinner Assembly: Summary
Spinner Assembly redesign was successful
Meets volume, data transmission and pointing knowledge requirements
Next Step: Selection of Space Rated Components