(Message inbox:218)
Received: from ATHENA.MIT.EDU by po5.MIT.EDU (5.61/4.7) id AA24686; Tue, 21 Apr 92 15:13:49 -0400
Received: from FINN.MIT.EDU by Athena.MIT.EDU with SMTP
	id AA03395; Tue, 21 Apr 92 15:13:09 EDT
From: pbh@Athena.MIT.EDU
Received: by finn.MIT.EDU (5.61/4.7) id AA00230; Tue, 21 Apr 92 15:12:56 -0400
Message-Id: <9204211912.AA00230@finn.MIT.EDU>
To: shabby@Athena.MIT.EDU
Subject: LWP4DOS info
Date: Tue, 21 Apr 92 15:12:52 EDT

Novell TCP/IP Transport for DOS OEM Guide 

TABLE OF CONTENTS

Introduction 
   TCP/IP files 
   ODI driver set 
   IPXODI.COM 

File descriptions 

Installing TCP/IP Software 
   Installation Procedure 
   Memory required for installation 
   Disk space required for installation 
   SHARE cannot be running during installation 

Programs 
   TCPIP.EXE 
      Sample Protocol section of NET.CFG configured for TCPIP: 
      Sample Link Support Layer (LSL) configuration section for default NET.CFG: 
   NETSTAT.EXE 
      Sample default NETSTAT output: 
      Sample  -E workstation summary output: 
      Sample NETSTAT -T SOCKET output: 
   PING.EXE 
      Sample PING command sequence: 
   IPTUNNEL.EXE 
      Sample NET.CFG for an IP Tunnel configuration: 
   RFCNBIOS.EXE 
      Sample Protocol section of NET.CFG with RFC NetBIOS parameters: 
      Initializing the RFC NetBIOS name table 
      Sample Protocol section of NET.CFG for RFCNBIOS: 
   VTCPIP.386 
   WLIBSOCK.DLL 

Database Files 
   LWP.INI 
      Sample [LANWorkPlace] section of LWP.INI file: drive:\WINDOWS\LWP.INI: 
   HOSTS 
      Sample HOSTS file: drive:\XLN\TCP\HOSTS: 
   RESOLV.CFG 
      Sample RESOLV.CFG file: drive:\XLN\TCP\RESOLV.CFG: 
   SERVICES 
      Sample SERVICES file: drive:\XLN\TCP\SERVICES: 
   NETWORKS 
      Sample NETWORKS file: drive:\XLN\TCP\NETWORKS: 
   PROTOCOL 
      Sample PROTOCOL file: drive:\XLN\TCP\PROTOCOL: 
   EXCELAN environment variable 

Configuration 
   NET.CFG options 
      Link Driver section 
      Hardware options 
      Software options 
      Link Support Section 
      Protocol Section 
   Sample Configuration Files 
      Sample NET.CFG file for Ethernet using an NE2000 board with Ethernet_II
        frame format: 
      Sample NET.CFG file for Ethernet using an NE2000 board and IPX with
        802.3 format: 
      Sample NET.CFG file for Token-Ring using IPX with 802.2 format: 
      Sample NET.CFG file for ARCnet using a TRXNET board with
        NOVELL_RX-NET format: 
   Sample System Files 
   Recommended AUTOEXEC.BAT file: drive:\AUTOEXEC.BAT: 
   Sample SYSTEM.INI file: drive:\WINDOWS\SYSTEM.INI: 
   Sample LWP.INI file: drive:\WINDOWS\LWP.INI: 




LIST OF TABLES:

Table 1. TCP/IP and Documentation files
Table 2. LAN Drivers in the ODI Driver Set
Table 3. NET.CFG parameters for the TCPIP program
Table 4. NET.CFG parameters for IP Tunnel
Table 5. NET.CFG parameters for RFC NetBIOS
Table 6. Most Frequently Used Link Driver Parameters
Table 7. Frame Types and Corresponding Network Types










                    NOVELL TCP/IP TRANSPORT FOR DOS OEM GUIDE
                    =========================================



                                INTRODUCTION
                                ============

The Novell TCP/IP Transport for DOS OEM package includes the following:


  >  Transmission Control Protocol/Internet Protocol (TCP/IP) files
  >  Open Datalink Interface (ODI) driver set
  >  Internetwork Packet Exchange (IPX) file for ODI, the IPXODI.COM file


This OEM guide describes the installation of this package, the purposes of
each transport utility, and how to configure the transport software for
Ethernet, Token-Ring, and ARCnet networks.



TCP/IP files
============

The TCP/IP files are a collection of transport utilities and related files.
The transport utilities are TCPIP, NETSTAT, PING, IPTUNNEL, and RFCNBIOS.
The related files include the HOSTS, SERVICES, NETWORKS, and PROTOCOL database
files; the NET.CFG and RESOLV.CFG configuration files; the VTCPIP.386 and
WLIBSOCK.DLL Windows support files; and an ASCII version of this guide, the
OEMGUIDE.TXT file. The TCP/IP files are described in detail throughout this
guide. Some sample system files (AUTOEXEC.BAT, SYSTEM.INI, and LWP.INI) are
also provided.



ODI driver set
==============

The ODI driver set supports multiple protocols and multiple network boards
on a single workstation. You configure the ODI drivers that you run on your
workstation by setting various parameters in the NET.CFG file.
The ODI driver set includes the following:


  >  The link support layer (LSL) driver (LSL.COM)

  >  Novell drivers (EXOS.COM, NE1000.COM, NE1500T.COM, NE2000.COM, NE2100.COM,
     NE2.COM, NE2-32.COM, and NE3200.COM)

  >  3Com drivers (3C501.COM, 3C503.COM, 3C505.COM, and 3C523.COM)

  >  A Token-Ring driver (TOKEN.COM)

  >  An ARCnet driver (TRXNET.COM)

  >  Miscellaneous network drivers and utilities (PCN2L.COM, LANSUP.COM,
     and ROUTE.COM)


The ODI driver set is described in this guide. Refer to the documentation
that came with your network board for additional information.



IPXODI.COM
==========

The IPXODI.COM file is the Novell IPX communication protocol for the ODI
driver set. The IPXODI.COM file is the protocol stack required when
running the NetWare shell.






                             FILE DESCRIPTIONS
                             =================

The TCP/IP and documentation files are listed in Table 1. Each file is
explained in this guide.



Table 1



TCP/IP and Documentation Files
------------------------------------------------------------------------------
File                        Description 
==============================================================================
OEMGUIDE.TXT                An ASCII version of this document
OEMGUIDE.DOC                A Microsoft Word 5.0 version of this document
XLN\BIN40\TCPIP.EXE         The TCP/IP transport program
XLN\BIN40\NETSTAT.EXE       The TCP/IP statistics program
XLN\BIN40\PING.EXE          The Internet Control Message Protocol (ICMP) echo
                            request program 
XLN\BIN40\IPTUNNEL.EXE      The IP Tunnel program for encapsulating IPX packets
                            within IP packets 
XLN\BIN40\RFCNBIOS.EXE      The RFC NetBIOS program 
XLN\BIN40\VTCPIP.386        The Windows 3.0 virtual device driver 
XLN\BIN40\WLIBSOCK.DLL      The Windows 3.0 socket library DLL
XLN\SAMPLE\HOSTS            The sample HOSTS database file
XLN\SAMPLE\RESOLV.CFG       The sample Domain Name Server's database file 
XLN\SAMPLE\NET.CFG          The sample NET.CFG configuration file 
XLN\TCP\SERVICES            The SERVICES database file
XLN\TCP\NETWORKS            The NETWORKS database file
XLN\TCP\PROTOCOL            The PROTOCOL database file
 
------------------------------------------------------------------------------
 


The miscellaneous LAN driver files in the ODI driver set are listed in Table
2. Each file is explained in the indicated vendor's documentation.



Table 2



LAN Drivers in the ODI Driver Set
------------------------------------------------------------------------------
LAN Driver    Used with Board or Program  Network Type  Hardware Vendor
==============================================================================
EXOS.COM      Novell EXOS205 and EXOS215  Ethernet      Microdyne 
LANSUP.COM    IBM LAN Support program     Token-Ring    IBM 
NE1000.COM    Novell Ethernet NE1000      Ethernet      Anthem
NE1500T.COM   Novell Ethernet NE1500T     Ethernet      Anthem
NE2000.COM    Novell Ethernet NE2000      Ethernet      Anthem
NE2100.COM    Novell Ethernet NE2100      Ethernet      Anthem
NE2.COM       Novell Ethernet NE2         Ethernet      Anthem
NE2-32.COM    Novell Ethernet NE2-32      Ethernet      Anthem
NE3200.COM    Novell Ethernet NE 3200     Ethernet      Anthem
PCN2L.COM     IBM PC Network II and II/A  Ethernet      IBM 
TOKEN.COM     IBM Token-Ring              Token-Ring    IBM 
TRXNET.COM    Novell RX-Net
              and Turbo RX-Net            ARCnet        Novell
ROUTE.COM     IBM Token-Ring              Token-Ring    IBM 
3C501.COM     3COM Etherlink 3C501        Ethernet      3Com
3C503.COM     3COM Etherlink 3C503        Ethernet      3Com
3C505.COM     3COM Etherlink 3C505        Ethernet      3Com
3C523.COM     3COM Etherlink 3C523        Ethernet      3Com
------------------------------------------------------------------------------







                       INSTALLING THE TCP/IP SOFTWARE
                       ==============================

This section describes the installation procedure, the disk space and memory
requirements, and provides a warning about the MS/DOS SHARE.EXE utility.



Installation procedure
======================

Follow these steps to install the Novell TCP/IP Transport for DOS software:

1. Gather the following information for installation:


   Target drive for TCP/IP software: _________________________________________

   Internet address of your workstation: _____________________________________

   Internet subnetwork mask (if subnetworks exist): __________________________

   Internet router address (if applicable): __________________________________

   Domain name, if using Domain Name Server: _________________________________

   Domain Name Server's IP address (if applicable): __________________________

   Network board, make and model: ____________________________________________


2. Install the TCP/IP Transport for DOS software.

To install the software, insert the TCP/IP Transport diskette into drive A:
and type the following:

                       C:\>   A:INSTALL   [-M] 

where the -M option is used for a workstation that has a color display
adapter and a monochrome monitor. If you select Yes when the installation
program asks if you want your system files updated, the program makes copies
of the existing AUTOEXEC.BAT, NET.CFG, and SYSTEM.INI, with the
extension.SAV. If you select No, the program creates updated system files
with the.LWP extension and you must update your system files manually to
ensure that they contain the lines required to run the TCP/IP Transport for DOS
software.
The DOS prompt appears after the installation program ends. You can
reboot your workstation and load  TCP/IP Transport for DOS applications
except in the following cases:


 You have changed the default hardware settings on your network board. In this
 case, you must edit your NET.CFG file, and change the entries in the Link
 Driver section associated with your board. These may include
 the interrupt number (INT), the port (PORT), direct memory access (DMA), and
 the memory base (MEM).

 You are using the TCP/IP Transport for DOS software and NetWare
 (IPX protocols), and you have modified the NetWare default protocol type
 with the ECONFIG utility. In this case, refer to the Sample Configuration
 Files section in this guide for a sample NET.CFG file for using an NE2000
 board with Ethernet_II frame format, and then make the appropriate changes
 to this file on your workstation.



Memory required for installation
================================

The TCP/IP for DOS installation program requires at least 400 kilobytes to
install on a workstation that does not already have TCP/IP transport
installed. The program requires 425 kilobytes of available memory if you are
upgrading your workstation.
This is memory available to programs after your workstation has started. If
you have less than this amount free, the installation program may fail to
install the software properly. You can check your available memory by using
the DOS CHKDSK command.
If the installation program terminates with an error message indicating a
lack of memory, or if there are files with the extension .ERR in the
directory \XLN\INSTALL indicating a lack of memory, you must make more
memory available for the installation program. You can make more memory
available by temporarily removing device drivers from your CONFIG.SYS
file and temporarily removing commands that start terminate-and-stay-resident
(TSR) programs from your AUTOEXEC.BAT file.



Disk space required for installation
====================================

The installation program requires 1.2 megabytes of free disk space to
install the TCP/IP software. The installation program will detect if you do
not have enough free disk space on your selected drive, but it will let you
continue if you are re-installing to upgrade your software.





SHARE cannot be running during installation
===========================================

The installation program will detect if the MS/DOS SHARE.EXE utility is
running when you enter A:INSTALL. To unload SHARE.EXE, reboot your
workstation. To prevent SHARE.EXE from being loaded, you may have to rename
the file temporarily before running the installation program.



                                  PROGRAMS
                                  ========

This section describes the TCPIP, NETSTAT, PING, IPTUNNEL, and RFCNBIOS
programs and the Windows support files VTCPIP.386 and WLIBSOCK.DLL. This
description includes the following information:


  >  Sample output from the PING and NETSTAT programs 

  >  Instructions for configuring the TCPIP, IPTUNNEL, and RFCNBIOS programs by
     setting parameters in the NET.CFG file

  >  Instructions for loading the VTCPIP.386 device driver to let both DOS and
     Windows use the TCPIP program

  >  The function of the WLIBSOCK.DLL file





TCPIP.EXE
=========


Syntax:


TCPIP [-U] [-C=filename] [-H]

Description: 


The TCPIP utility loads the TCP/IP protocol stack into memory. The LSL and
an appropriate MLID must be loaded into memory before TCPIP will load. TCPIP
must be loaded before any TCP/IP-based applications (for example, LAN
WorkPlace for DOS) will operate.
The NET.CFG file contains several parameters that modify the configuration
and behavior of TCP/IP.



Options and Parameters: 


-U

You can unload the TCP/IP protocol from memory by using the ---U option in
the command line.

-C=filename

Normally, the LSL.COM program on your local system uses the same  NET.CFG
file as TCP/IP.  If configuration requirements warrant, you can use the -C
option to specify a different NET.CFT file.  The -C option lets you specify
the full path to the NET.CFG file that TCPIP.EXE should use to obtain
configuration information. 

If you do not use the -C option, TCPIP.EXE uses the same NET.CFG file that
the LSL.COM program reads when the LSL is loaded.

-H

The -H option provides command-line help information.





------------------------------------------------------------------------------
NOTE:
The hyphen (-) preceding the option can be replaced by a slash (/).
------------------------------------------------------------------------------

For example:

     TCPIP -C=F:\USER\MARILYN\NET.CFG

is equivalent to

     TCPIP /C=F:\USER\MARILYN\NET.CFG

This is true for all TCP/IP transport program options.



Samples:




The NET.CFG parameters for TCP/IP are explained in Table 3. The samples that
follow show a Protocol section with NET.CFG parameters set for using the
TCPIP program and a sample Link Support section with the default
NET.CFG settings.



Table 3



NET.CFG Parameters for the TCPIP Program
------------------------------------------------------------------------------
Parameter     Description 
==============================================================================
ip_address    The IP address of this workstation. If this keyword is not
              present or contains the value 0.0.0.0, then TCPIP tries to use
              RARP to determine the local IP address. 

ip_router     The IP address of a remote system that acts as a router to other
              IP networks. If this keyword is not present, then TCPIP is unable
              to send packets to systems on other networks.

ip_netmask    The subnetwork mask for this workstation. In all of the NET.CFG
              samples in this document, we  use a Class B address with a 16-bit
              network address and a 16-bit host portion. The host portion
              consists of 6 bits of subnet address and 10 bits of host address. 

tcp_sockets   The number of concurrent TCP connections. The default value is 8.
              The maximum value is 64.

udp_sockets   The number of concurrent UDP connections. The default value is 8.
              The maximum value is 32.

raw_sockets   The number of concurrent RAW IP connections. The default value
              is 8. The maximum value is 8. This value must be at least 1 if
              you use the PING program. 
 
------------------------------------------------------------------------------




Sample 
-------

Protocol section of NET.CFG configured for TCPIP:
-------------------------------------------------




------------------------------------------------------------------------------
 Protocol TCPIP
   ip_address                    144.52.6.5
   ip_router                     144.52.6.6
   ip_netmask                    255.255.252.0
   tcp_sockets                   8
   udp_sockets                   8
   raw_sockets                   1
------------------------------------------------------------------------------



The TCPIP program uses packet buffers and memory services provided by the
LSL.COM program. TCP/IP is configured by setting the 'Buffers' and 'Mempool
'parameters in the Link Support section of the NET.CFG file.

The minimum number of 'Buffers' required by TCPIP is 1. The default value is
8. Increasing the number of 'Buffers' may lead to better performance.
Decreasing the number of 'Buffers' leads to smaller memory requirements.

The minimum size of the 'MemPool' required by TCPIP is 1024 bytes. The
default value is 4096 bytes. Increasing the 'MemPool' size may lead to
better performance. Decreasing the 'MemPool' size leads to smaller
memory requirements.



Sample Link Support Layer (LSL) configuration section for default NET.CFG:
--------------------------------------------------------------------------




------------------------------------------------------------------------------
 Link Support
      Buffers 8 1500
      MemPool 4096
------------------------------------------------------------------------------




NETSTAT.EXE
===========


Syntax: 


NETSTAT[-E]  [-H] [-T [table_type] [-P protocol]]
[-F [output_format]] [-I [socket_id]]
[-N] [node_name]

Description: 


The NETSTAT utility lets you retrieve and examine local and remote statistics
and configuration information. With NETSTAT, you can determine if a remote
node is configured and operating properly. 
NETSTAT displays the contents of various network-related data structures in
various formats, depending on the options you select.
NETSTAT displays either remote-access status for a target host if the target
is remote, or local-access status if the specified target host is your
workstation (the default value).

Options and Parameters: 


-E
Displays the Internet address, MAC address, IP subnet mask, network number,
default router, and the number of TCP, UDP, and raw sockets.

-T [table_type]
Specifies the table to display. The available table types are as follows:

   arp       ARP table
   route     Route table
   socket    Socket table
   stat      Statistics table
   pcmib     PCMIB table

The default 'table_type' is STAT. 





------------------------------------------------------------------------------
NOTE:
The -P, -F and -I options are valid only when the '-T socket' option
is specified. If the -P, -F, or -I options are specified without the
'-T socket' parameter, they are ignored.

-------------------------------------------------------------------------------

P [protocol]

Specify the protocol of the sockets to be displayed; 'protocol' can be one
of the following values:

   tcp  Show TCP sockets.
   udp  Show UDP socket.
   raw  Show RAW sockets.

The default protocol is TCP. The -P option is only valid with the '-T socket'
parameter.


-F [output_format]
Specify the format of the socket output; 'output_format' can be one of the
following values:

   terse     Display abbreviated summary.
   verbose   Display full socket information.

The default 'output_format' is TERSE. The -F option is only valid with the '-T
socket' parameter.


-I [socket_id]
Specifies the socket to show statistics about; 'socket_id' has the following
value:

    soid    The ID of the socket required

If you omit the 'socket_id', NETSTAT displays a terse version of all active
sockets. The -I option is only valid with the '-T socket' parameter.


-H
The -H option provides command-line help information.


-N node_name

Specify the target node for retrieving NETSTAT information. The 'node_name'
can be either a valid Internet address or a name of any node running the
TCP/IP Transport for DOS software. If the -N parameter is used, a 'node_name'
must be specified.


Samples:
The following samples show the default NETSTAT packet activity output,
the NETSTAT -E workstation summary output, and a NETSTAT -T socket table.

Sample default NETSTAT output:
------------------------------


------------------------------------------------------------------------------
                          IP          ARP
Transmitted Packets:     303           15
Received Packets:       2295         4233
Dropped Packets:           0           17
------------------------------------------------------------------------------





Sample NETSTAT -E workstation summary output:
---------------------------------------------




------------------------------------------------------------------------------
TCP sockets         = 8
UDP sockets         = 8
RAW sockets         = 1
IP Address          = 144.52.6.5 
IP Net Mask         = 255.255.252.0
Local Net           = 144.52.0.0
Default Router      = 144.52.6.6
MAC Address         = 00-00-1b-02-a0-09
TCP/IP Version      = 4.01

------------------------------------------------------------------------------






Sample NETSTAT -T SOCKET output:
--------------------------------


------------------------------------------------------------------------------
soid    proto sendq recvq  local_addr           remote_addr           state
01      tcp    0     0     144.52.6.5:echo       0.0.0.0:0            LISTEN
02      tcp    0     0     144.52.6.5:discard    0.0.0.0:0            LISTEN
03      tcp    0     0     144.52.6.5:chargen    0.0.0.0:0            LISTEN
04      tcp    0     0     144.52.6.5:1025       130.57.6.3:telnet    ESTABLISHED
05      tcp    0     0     144.52.6.5:discard    130.57.6.2:1026      ESTABLISHED
09      udp    0     0     144.52.6.5:echo       0.0.0.0:0
10      udp    0     0     144.52.6.5:discard    0.0.0.0:0
11      udp    0     0     144.52.6.5:chargen    0.0.0.0:0
------------------------------------------------------------------------------






PING.EXE
========


Syntax: 


PING [-D delay_time] [-N numpackets] [-S size] [-H] node_name

Description: 


The PING utility sends Internet Control Message Protocol (ICMP) echo packets
to the network host specified. PING uses the ICMP protocol's mandatory echo
request datagram to get an echo response from the specified host or
network router.

Options and Parameters: 


-D delay_time
The number of seconds between successive ICMP echo requests. The default
delay is 1 second.


 -N numpackets
The number of ICMP echo requests to send.  If you don't specify the number
of packets to send, PING continues sending packets until you get a response
or enter Ctrl-C.


-S size
The size of ICMP echo requests to send. The default 'size' is 56 data bytes
(a 64-byte record with 8 bytes for the header).


-H
The -H option provides command-line help information.


node_name
The specified node or network router. This value can be a name or an
Internet address. If the 'node_name' is given a valid Internet name, the
PING packet is sent across the Internet.


Samples


The following samples illustrate the standard ICMP responses to the PING
query.

Sample PING command sequence:
-----------------------------


Input:


PING SUPPORT.MYCOMPANY.COM

Output (successful):


 support.mycompany.com is alive

Output (unsuccessful because host name is not valid):


 ping: unknown host support.mycompany.com

The above response indicates that your hosts file or DNS could not resolve
the IP address for the given host or the host does not exist.

Output (unsuccessful because host is down):


 ping: no answer from support.mycompany.com

The above response indicates that the host is not on the Internet and
running TCP/IP, is not currently reachable, or does not exist.





IPTUNNEL.EXE
============


Syntax: 


IPTUNNEL [-U] [-H]

Description: 


The IPTUNNEL program lets a NetWare DOS client communicate with a NetWare
server that is only accessible through an IP internet. Normally, an IP
Tunnel connection is installed between two or more NetWare servers on a
TCP/IP internet. In such a configuration, a NetWare client that is connected
to one of these servers does not need to use the IPTUNNEL program to access
the remote servers.

Options and Parameters: 


-U
The IPTUNNEL module can be unloaded from memory by using the -U option in the
command line. 


-H
The -H option provides command-line help information.

Sample


The NET.CFG parameters for IP Tunnel are described in Table 4. The samples
that follow illustrate a typical IP Tunnel configuration.



Table 4



NET.CFG Parameters for IP Tunnel
------------------------------------------------------------------------------
Parameter     Description 
==============================================================================

gateway       Specifies the IP address of the remote NetWare server
              (running v3.11 or later). A maximum of 10 gateways can be
              configured. The gateway address of each peer server in an IP
              Tunnel configuration must be listed. 
 
port          Sets the UDP port value used by IPTUNNEL.EXE. The default value
              is 213. Older versions of the Schneider & Koch SK-IPX/IP
              products for NetWare 2.x use a UDP port value of 59139.

checksum      Normally, the IP Tunnel places a UDP checksum on every packet
              it transmits. Setting 'checksum' to No disables UDP checksum
              calculations. The recommended setting is Yes.
 
------------------------------------------------------------------------------




Sample NET.CFG for an IP Tunnel configuration:
----------------------------------------------



------------------------------------------------------------------------------
Link Support
     Buffers 8 1500
     MemPool 4096

Link Driver IPTUNNEL
     gateway              144.52.66.50
     gateway              149.32.1.100
     port                 213
     checksum             yes

Link Driver NE2000
     Frame Ethernet_II

Protocol IPX
     Bind IPTUNNEL

Protocol TCPIP
     ip_address           144.52.6.5
     ip_router            144.52.6.6
     ip_netmask           255.255.252.0
------------------------------------------------------------------------------




------------------------------------------------------------------------------
NOTE:
The program-loading order when using the client IP Tunnel is as follows:

LSL
NE2000 (or the ODI driver for your network board)
TCPIP
IPTUNNEL
IPX
ODI
NETX
------------------------------------------------------------------------------





RFCNBIOS.EXE
============


Syntax: 


RFCNBIOS [-U]

Description: 


The RFCNBIOS utility lets any program that uses the software interrupt 5CH
programming interface use the TCP/IP Transport. RFCNBIOS is a TSR program.
It provides a NetBIOS (Network Basic Input Output System) interface
compliant with RFC1001 and RFC1002. 

RFCNBIOS reads its configuration parameters from the Protocol section of the
NET.CFG file.

Options and Parameters: 


-U
You can use the -U option from the command line to unload  the RFCNBIOS
module  from memory. 



Sample


The NET.CFG parameters for RFC NetBIOS are explained in Table 5. The sample
that follows illustrates a Protocol section of NET.CFG for RFC NetBIOS.



Table 5



NET.CFG Parameters for RFC NetBIOS
------------------------------------------------------------------------------
Parameter     Description 
==============================================================================

nb_sessions   Specifies the maximum number of concurrent RFC NetBIOS sessions.
              NOTE: The 'tcp_sockets' parameter must be at least
              'nb_sessions' + 1. The default value for 'nb_sessions' is 4; the
              maximum value is 64.
 
nb_commands   Specifies the maximum number of asynchronous RFC NetBIOS commands.
              Each pending NetBIOS command requires 32 bytes of memory. The
              default value for 'nb_commands' is 8; the maximum value is 64. 

nb_adapter    Specifies the NetBIOS board number. This value must be either 0
              or 1. The default value is 0. 

nb_brdcast    Specifies the format of the IP broadcast address used when
              performing NetBIOS name transactions. The default value of 1
              indicates that the all-ones style of IP broadcast address should
              be used. If you have difficulty interoperating with another
              vendor's implementation of RFC NetBIOS, you might try changing
              the 'nb_brdcast' to 0.

nb_domain     Specifies the name of the NetBIOS workgroup this workstation
              belongs to. The recommended practice is to omit the 'nb_domain'
              parameter. 
 
------------------------------------------------------------------------------




Sample Protocol section of NET.CFG with RFC NetBIOS parameters:
---------------------------------------------------------------




------------------------------------------------------------------------------
Protocol TCPIP
   ip_address          144.52.6.5
   ip_router           144.52.6.6
   ip_netmask          255.255.252.0
   tcp_sockets         8
   udp_sockets         8
   raw_sockets         1
   nb_sessions         4    # Begins RFCNBIOS parameters
   nb_commands         8
   nb_adapter          1
   nb_brdcast          1    # Ends RFCNBIOS parameters

------------------------------------------------------------------------------




Initializing the RFC NetBIOS name table
---------------------------------------

The RFC NetBIOS name table can be initialized with up to 16 names and remote
IP addresses. The Protocol RFCNBIOS section should only be used if you need
to access remote RFC NetBIOS nodes that are not on the same broadcast
network as your workstation.

Sample Protocol section of NET.CFG for RFCNBIOS:
------------------------------------------------




------------------------------------------------------------------------------
Protocol RFCNBIOS
    name1                 144.52.15.9
    netname2              144.52.15.6
------------------------------------------------------------------------------



VTCPIP.386
==========

The VTCPIP.386 file contains a Windows 3.0 virtual device driver that lets
both DOS and Windows programs access the services provided by the TCPIP.EXE
TSR. Windows 3.0 will load the VTCPIP.386 driver only when operating in
enhanced mode. The DEVICE= setting must be added to the [386Enh] section
of the Windows SYSTEM.INI file in order to tell Windows to load VTCPIP.386.
For example:

[386Enh]DEVICE=VTCPIP.386.

The above statement requires that the VTCPIP.386 device driver must be
located in a directory specified in the PATH environment variable or in the
SYSTEM subdirectory in the Windows directory.





------------------------------------------------------------------------------
NOTE:
If you have installed the TCP/IP Transport for DOS software, then your
SYSTEM.INI file should already contain this line.
------------------------------------------------------------------------------




WLIBSOCK.DLL
============

The WLIBSOCK.DLL file contains the Windows 3.0 Socket Library DLL. This
DLL lets Windows 3.0 application programs use the TCPIP.EXE TSR. 

WLIBSOCK.DLL works with all 3 modes of Windows 3.0: real, standard, and
enhanced. When running under Windows 3.0 in enhanced mode, WLIBSOCK.DLL uses
the VTCPIP.386 driver to access TCPIP.EXE.

The WLIBSOCK.DLL file must be located in a directory specified in the PATH
environment variable.



                               DATABASE FILES
                               ==============

The Novell TCP/IP Transport for DOS database files include the HOSTS,
SERVICES, NETWORKS, and PROTOCOL files. These files provide the categories
for organizing the key components needed for effective database management.
These files are augmented by two additional files: LWP.INI and
RESOLV.CFG. The LWP.INI file enables the socket library DLL to find these
database files. The RESOLV.CFG configuration file lets you identify up to
three domain name servers.



LWP.INI
=======



A Windows 3.0 user needs an LWP.INI file in the WINDOWS directory in order
for the WLIBSOCK.DLL library to find the paths to the database files. If you
have already installed the Novell LAN WorkPlace for DOS software (not
included in the OEM package), then this file should already be in your
WINDOWS directory.

Sample [LANWorkPlace] section of LWP.INI file: "drive":\WINDOWS\LWP.INI:
------------------------------------------------------------------------




------------------------------------------------------------------------------
[LANWorkPlace]

ROOT=C:\XLN; Product root directory
; NOTE: The LAN WorkPlace for DOS programs require many other 
;       entries, but the TCP/IP transport only requires 
;       the ROOT entry.
------------------------------------------------------------------------------






HOSTS
=====

The HOSTS file specifies a table of remote host names and their IP addresses. 



------------------------------------------------------------------------------
NOTE:
You do not need a 'localhost' entry in the HOSTS file to assign
an IP address to your workstation. Your local IP address is specified in your
NET.CFG file.
------------------------------------------------------------------------------


Sample HOSTS file: "drive":\XLN\TCP\HOSTS:
------------------------------------------




------------------------------------------------------------------------------
# IP Address     name and optional aliases

144.52.6.1       sales sa
144.52.6.2       marketing ma
144.52.6.3       engineering en
144.52.6.4       support su
------------------------------------------------------------------------------



------------------------------------------------------------------------------
NOTE:
Copy the HOSTS file from the SAMPLE directory (\XLN\SAMPLE) to the TCP directory
(\XLN\TCP), and then edit it list the available hosts on your network.
------------------------------------------------------------------------------




RESOLV.CFG
==========



The RESOLV.CFG file contains the domain name and domain name server IP
addresses for use with the Domain Name Service (DNS). You can specify a
maximum of 3 domain name server addresses in the RESOLV.CFG file.





------------------------------------------------------------------------------
NOTE:
If your site does not have a DNS server, then you should delete
the RESOLV.CFG file or rename it to another name such as RESOLV.OFF.
------------------------------------------------------------------------------




Sample RESOLV.CFG file: "drive":\XLN\TCP\RESOLV.CFG:
----------------------------------------------------


------------------------------------------------------------------------------
domain     company.com
nameserver 144.52.6.16
nameserver 144.52.8.32 
------------------------------------------------------------------------------








------------------------------------------------------------------------------
NOTE:
Copy the RESOLV.CFG file from the SAMPLE directory (\XLN\SAMPLE) to the TCP
directory (\XLN\TCP), and then edit it to include the domain name servers on
your network.
------------------------------------------------------------------------------




SERVICES
========

The SERVICES file provides a way to convert string representations of
network services to their strings  corresponding well-known TCP or UDP port
number (for example, echo converts to port 7). Most applications use the
well-known port number instead of referencing this file, so the SERVICES
file is generally not required.

Sample SERVICES file: "drive":\XLN\TCP\SERVICES:
------------------------------------------------

 
------------------------------------------------------------------------------

# Service Name  Port/Protocol       Aliases
echo                7/tcp
discard             9/udp           sink null 
chargen            19/tcp           ttytst source
telnet             23/tcp

------------------------------------------------------------------------------


 





NETWORKS
========

The NETWORKS file lists network names (for example, ARPANET and MILNET) and
their corresponding network numbers.

Sample NETWORKS file: "drive":\XLN\TCP\NETWORKS:
------------------------------------------------

 
------------------------------------------------------------------------------

# Name          Network Number
ournet          144.52
arpanet         10
milnet          26

------------------------------------------------------------------------------






PROTOCOL
========

The PROTOCOL file lists the known protocols, their corresponding IP protocol
numbers, and any aliases for those protocols for your network.

Sample PROTOCOL file: "drive":\XLN\TCP\PROTOCOL:
------------------------------------------------




------------------------------------------------------------------------------

# Name Number Aliases
icmp    1     ICMP  # internet control message protocol
tcp     6     TCP   # transmission control protocol
udp     17    UDP   # user datagram protocol

------------------------------------------------------------------------------






EXCELAN environment variable
============================

The EXCELAN environment variable is used to locate various database files
that may be needed to run your networking applications. All database files
must be located in the same directory, and the directory name must be TCP.
The default location of the database files is drive:\XLN\TCP, and the
default value of the EXCELAN environment variable is drive:\XLN.
This environment variable should be set in your AUTOEXEC.BAT file.  If you
do not set this variable, then the transport assumes that  your
database files are located in C:\XLN\TCP. 





                               CONFIGURATION
                               =============

Configuration of the TCP/IP transport is done by setting options in the
NET.CFG file. This section describes the NET.CFG options that can be used to
configure the TCP/IP transport; the Link Driver,  and provides sample
NET.CFG files for some of the more frequent configurations.



NET.CFG options
===============

You can use the NET.CFG file to change specific hardware settings on your
network board or to set up your workstation for multiple protocols. You may
need to refer to the documentation for your network board or for the
protocol you are using for additional NET.CFG information.

Main section headings in the NET.CFG file must be left-justified and must
precede the options you include in a section. Options are listed under each
heading and indented with a tab or at least one space. Section headings and
options are not case sensitive. Precede comments with a number sign (#) or
semicolon (;). End each line with a hard return. Write all numbers in
decimal notation except where noted otherwise.You can use any DOS text
editor to create or edit the file.

This section describes the NET.CFG options and how to use them.
The following conventions are used:

   [ ]      An optional element
   number   A decimal number
   hex      A hexadecimal number

Typical configurations of the TCP/IP transport include the following
NET.CFG sections:


  >  Link Driver

  >  Protocol

  >  Link Support




The following paragraphs describe these configuration sections and the
options for each section.



Link Driver section
===================

The Link Driver section is used for naming your driver and specifying
various hardware and software settings for this driver. The Link Driver
section has the following format:

Link Driver drivername

  INT   [#1 | #2] interrupt_request_number
  PORT [#1 | #2] hex_starting_address hex_number_of_ports
  DMA [#1 | #2] channel_number
  MEM [#1 | #2] hex_starting_address [hex_length]
  SLOT number
  CONNECTOR DIX
  NODE ADDRESS hex_address
  FRAME frame_type
  PROTOCOL name hex_protocol_ID frame_type
  SAPS number
  LINK STATIONS number
  ALTERNATE
  MAX FRAME SIZE number

Table 6 identifies the Link Driver parameters that are used most frequently
when configuring LAN drivers. The following legend is used in this table:


  >  ISA indicates industry standard architecture.

  >  MCA indicates Micro Channel architecture.

  >  Both indicates that the option is available with the ISA and MCA
     architectures.

  >  EISA indicates extended industry standard architecture.


  >  The  characters  --  indicate that the option is not available for the
     indicated driver.



Table 6



Most Frequently Used Link Driver Parameters
------------------------------------------------------------------------------
LAN Driver    DMA           INT           MEM           PORT          SLOT
==============================================================================
EXOS.COM      --            ISA           ISA           ISA           MCA 
LANSUP.COM    --            --            --            --            --
NE1000.COM    --            ISA           --            ISA           --
NE1500T.COM   ISA           ISA           --            ISA           --
NE2000.COM    --            ISA           --            ISA           --
NE2100.COM    ISA           ISA           --            ISA           --
NE3200.COM    --            --            --            --            EISA
NE2.COM       --            --            --            --            MCA 
NE2-32.COM    --            --            --            --            MCA 
PCN2L.COM     --            --            --            --            MCA 
TOKEN.COM     --            --            --            --            MCA 
TRXNET.COM    --            ISA           ISA           ISA           MCA 
3C501.COM     --            ISA           --            ISA           --
3C503.COM     --            ISA           --            ISA           --
3C505.COM     ISA           ISA           --            ISA           --
3C523.COM     --            --            --            --            MCA 
                           
------------------------------------------------------------------------------








------------------------------------------------------------------------------
NOTE:

If you are using a LAN driver not listed in Table 6, refer to its
documentation for parameter applicability.
------------------------------------------------------------------------------


To use the Link Driver section, replace 'drivername' with the name of the
driver you are using; the 'drivername' is typically the LAN driver's
executable filename (for example, NE2000 for NE2000.COM).

Replace 'drivername' with one of the following driver names: 

 EXOS (for Novell EXOS205 and EXOS215)
 LANSUP (for the IBM LAN Support program only)
 NE2 (for Novell Ethernet NE/2) 
 NE2-32 (for Novell Ethernet NE/2-32) 
 NE1000 (for Novell Ethernet NE1000)
 NE1500T (for Novell Ethernet NE1500T)
 NE2000 (for Novell Ethernet NE2000)
 NE2100 (for Novell Ethernet NE2100)
 NE3200 (for Novell Ethernet NE3200)
 PCN2L (for IBM PC Network II and II/A)
 TOKEN (for IBM Token-Ring)
 TRXNET (for Novell RX-Net and Turbo RX-Net)
 3C501 (for 3Com EtherLink) 
 3C503 (for 3Com EtherLink Series II)
 3C505 (for 3Com EtherLink Plus)
 3C523 (for 3Com EtherLink/MC)

After specifying a 'drivername', place applicable hardware options and
software options under the Link Driver heading.

You can specify options for each network board you are using, but you must
have a separate Link Driver 'drivername' heading for each network board.



Hardware options for the Link Driver section
--------------------------------------------

The NET.CFG hardware options for the Link Driver section are as follows:

 INT   [#1 | #2] interrupt_request_number
 PORT [#1 | #2] hex_starting_address hex_number_of_ports
 DMA [#1 | #2] channel_numberMEM [#1 | #2] hex_starting_address [hex_length]
 SLOT number
 CONNECTOR DIX
 NODE ADDRESS hex_address

Each of these options is described in the following paragraphs. For the INT,
PORT, DMA, and MEM options, you do not need to include the characters "#1"
if you are specifying a value for only one network board. For example, if
you are using the first configurable DMA channel on a 3C505 board as DMA
channel 3, you can place the following lines in your NET.CFG file:

Link Driver 3C505
   DMA 3 

or

Link Driver 3C505
   DMA #1 3 

If, however, you are using more than one DMA, INT, PORT, or MEM value, you
must include the characters "# 2" for the second value. This abbreviation
convention is used for all NET.CFG options that use the [#1 | #2] notation.

INT [#1 | #2] 


interrupt_request_number


The INT option (called IRQ, for interrupt request, by some vendors) specifies
which interrupt your network board uses. For example, to specify interrupt 5
on an NE2000 board, place the following lines in your NET.CFG file:

Link Driver NE2000
  INT #1  5


To specify more than one 'interrupt_request_number', use the following
syntax in your NET.CFG file:

Link Driver XY5000
  INT #1 2
  INT #2 3 



DMA [#1 | #2] channel_number


The DMA (direct memory address) option specifies the hardware setting of the
network board used in the workstation. This option lets you configure DMA
channels by entering the 'channel_number' to be used. The default value is
the first configurable channel (#1). 

For example, if the first configurable DMA channel on your board uses
channel 3 and the second configurable channel uses channel 4, place the
following lines in your NET.CFG file:

 Link Driver XY4000
  DMA #1 3
  DMA #2 4


MEM [#1 | #2] 


hex_starting_address [hex_length]


The MEM option specifies a memory range to be used by the network board.

Use the hexadecimal physical (absolute) address of the memory used by the
board. This 'hex_starting_address' must match the starting address
configured on the board.

Enter the 'hex_length' in hexadecimal paragraphs (a paragraph is 16 bytes)
of the memory address range used by the board. For example, if you address a
board from D0000 to D4000 (bytes), the starting address is D0000 and the
range is 400 hexadecimal paragraphs. In this case, for an EXOS board (for
example, EXOS205), place the following lines in your NET.CFG file:

Link Driver EXOS
   MEM D0000  400


Usually, the length ('hex_length') is not needed.



PORT [#1 | #2] hex_starting_address [hex_number_of_ports]


Use the PORT option to specify the starting port ('hex_starting_address')
and the number of ports in the range ('hex_number_of_ports'). All values
must be written in hexadecimal notation.

For example, suppose you want to specify the starting port and the number of
ports in the first range on your board. The starting I/O port is 300; 16
ports are in the first range. Place the following lines in the NET.CFG file:

 Link Driver NE2000
 Port #1 300

The number of ports ('hex_number_of_ports') is optional. The following
example specifies two ranges with 32 ports in each range:

Link Driver 3C505

  Port #1 300 32
  Port #2 700 32



SLOT number

In slot-based computers, the driver usually locates the board by scanning
through the slots in order from lowest to highest. The SLOT option directs
the driver to eliminate the scan and locate the board in the specified slot.

Use the number of the slot into which you inserted the board. The slot
number is usually found on the back of the workstation. The LAN driver will
use the board in this slot.

For example, if you are using two NE2 boards in the same workstation and you
insert one board into slot 1 and the other into slot 2, place the following
lines in your NET.CFG file:

Link Driver NE2
  Slot 1
Link Driver NE2
  Slot 2


Then place the following lines in your batch file:

   LSL
   NE2
   NE2

The SLOT option directs the first NE2 driver to use the NE2 board in slot 1
and directs the second NE2 driver to use the NE2 board in slot 2.



CONNECTOR DIX


The CONNECTOR DIX option configures the 3C503 LAN driver to use the DIX
(thick) connector. BNC/TP (thin) is the default value. To specify the DIX
connector, for example, place the following lines in your NET.CFG file:

Link Driver 3C503
  CONNECTOR DIX

DIX can also be selected at the command line, as in the following example:

 3C503 /D



NODE ADDRESS 


hex_address


The NODE ADDRESS option overrides any hard-coded node addresses in the
network board, if the hardware allows it. Use the 'hex_address' parameter to
specify a hexadecimal address number.



------------------------------------------------------------------------------
NOTE:
Changing the node address on a board can create conflicts with other network 
boards. Use the hardware-based node address whenever possible.
------------------------------------------------------------------------------


The example below shows how to change the node address on a 3C523 board:

Link Driver 3C523
  NODE ADDRESS 12D43



Software options for the Link Driver section
--------------------------------------------

The NET.CFG software options for the Link Driver section are as follows:

Link Driver drivername
  FRAME frame_type
  PROTOCOL name hex_protocol_ID frame_type
  MAX FRAME SIZE number
  LINK STATIONS number
  SAPS number
  ALTERNATE



FRAME frame_type

The FRAME option enables the frame types used by the network board. Use this
option with network boards that support multiple frame types.

For example, to enable the Ethernet II frame type on an NE1000 board, place
the following lines in the NET.CFG file: 

  Link Driver NE1000
   FRAME ETHERNET_II 

The TCP/IP Transport for DOS software supports frame types Ethernet_II and
Ethernet_SNAP. For OSI, use frame type Ethernet_802.2. For IPX, Ethernet LAN
drivers default to the Ethernet_802.3 frame type; Token-Ring LAN drivers
default to the Token-Ring frame type.


Table 7 lists the supported network types for each NET.CFG frame type
parameter. The characters -- indicate that the network is not applicable for
the stated frame type.



Table 7



Frame Types and Corresponding Network Types
------------------------------------------------------------------------------
Frame Type    Ethernet      Token-Ring    ARCnet        IBM PC-NET
==============================================================================
ETHERNET_II   Supported     --            --            --
ETHERNET_SNAP Supported     --            --            --
ETHERNET_802.2              Supported     --            --            --
ETHERNET_802.3              Supported     --            --            --
TOKEN-RING_SNAP             --            Supported     --            --
TOKEN-RING    --            Supported     --            --
NOVELL_RX-NET --            --            Supported     --
IBM_PCN2_802.2              --            --            --            Supported 
IBM_PCN2_SNAP --            --            --            Supported 
             
------------------------------------------------------------------------------


PROTOCOL 


name  hex_protocol_ID  frame_type


The PROTOCOL option lets existing LAN drivers handle new network protocols.
Replace 'name' with the name of the new protocol.

Replace 'hex_protocol_ID' with the assigned hexadecimal protocol ID that the
protocol is assigned.

Replace 'frame_type' with the frame type that the new protocol ID applies to.


For example, if you want to use a new protocol XYZ with an NE2-32 network
board, the NET.CFG file would have the following lines:

Link Driver NE2-32 
  FRAME ETHERNET_SNAP 
  PROTOCOL XYZ 904A ETHERNET_SNAP 



MAX FRAME SIZE 


number


The MAX FRAME SIZE option sets the maximum number of bytes per packet that
can be put on the network by the LAN driver.

The TOKEN.COM driver's default size is 4216 bytes. But if your board has 8
KB of shared RAM available, the default size is 2168 bytes.

The LANSUP.COM driver's default is normally 1144 bytes. However, if you are
using the IBM LAN Support program with an Ethernet device driver, the
maximum size is 1496 bytes.

For TOKEN.COM and LANSUP.COM, the value for 'number' must be a multiple of
8. It must include the number of bytes for the data packet (usually 1, 2, 4,
or 8 KB), for network board overhead (6 bytes), and for the largest possible
header (currently, 35 bytes for the LAN header + 5 bytes for the SNAP header
+ 74 bytes for the protocol header = 114 bytes).

For 2 KB data packets, for example, the 'number' would be calculated as
follows:

           (data packet) +(header) +(constant)

                  2048   +  114    +   6  = 2168

If the above total is not a multiple of 8, then the TOKEN.COM driver will
round the total up to the next multiple of 8.

The NET.CFG file for a TOKEN Link Driver with a maximum frame size of 2168
would have the following lines:

Link Driver TOKEN
  MAX FRAME SIZE 2168







------------------------------------------------------------------------------
NOTE:
When the driver loads, the sign-on message does not reflect the 6 bytes of
overhead. Therefore, the MAX FRAME SIZE for the above example would be
displayed as 2162.
------------------------------------------------------------------------------

If the line speed is 16 Mbps, the value for 'number' can be between 632 and
17,960 bytes. If the line speed is 4 Mbps, the value for 'number' must be
between 632 and 4464 bytes.


LINK STATIONS number


If you use the LANSUP driver, you can specify the 'number' of link stations
needed. Set the LINK STATIONS option to allow for all applications using the
IBM LAN Support program. The maximum value depends on the type of board
used. The default value is 1 link station.





------------------------------------------------------------------------------
NOTE:
The LINK STATIONS option is ignored if another application has already opened
the board before the LANSUP.COM driver was loaded.
------------------------------------------------------------------------------


SAPS number


If you use the LANSUP driver, you can specify the 'number' of service access
points (SAPS) needed. Set the SAPS option to allow for all applications
using the IBM LAN Support program. The maximum value depends on the type of
board used. The default value is 1 service access point.





------------------------------------------------------------------------------
NOTE:
The SAPS option is ignored if another application has already opened the board
before the LANSUP.COM driver was loaded.
------------------------------------------------------------------------------




ALTERNATE


Normally, the LANSUP, Token-Ring, and PCN2L drivers have you specify a
primary board when you are using more than one board. Use the ALTERNATE
option if you want your driver to use the alternate board.

Specify ALTERNATE under the appropriate driver section heading, as
shown below:

Link Driver LANSUP
   ALTERNATE 




Link Support section
--------------------

The Link Support section is used for configuring receive buffers and the
size of the memory pool buffers. The Link Support section has the
following format:

Link Support
  BUFFERS number [size]
  MEMPOOL number

BUFFERS number [size]



The BUFFERS option configures the number and size of receive buffers to be
maintained by the Link Support Layer (LSL). The number of receive buffers
must be large enough to hold all media headers and the maximum data size.

The default number of buffers for the TCP/IP transport is 8. The default
buffer size is 1500 bytes. The minimum size is 618 bytes. The total buffer
space must fit into approximately 59 KB (space is the product of 'number'
times 'size'). The default settings use the following format:

Link Support
  BUFFERS 8  1500 


Refer to the documentation for other protocol stacks you are using for other
required settings.



MEMPOOL number


Some protocols use the MEMPOOL option to configure the size of the memory
pool buffers that the LSL will maintain. The MEMPOOL 'number' must be a
multiple of 1024 bytes.

The recommended MEMPOOL setting for the TCP/IP transport is 4096 bytes.

For example:

Link Support
   MEMPOOL 4096



The minimum MEMPOOL setting for the TCP/IP transport is 1024 bytes. Using a
larger value may improve performance when communicating with certain hosts.
Refer to the documentation for other protocol stacks you are using for other
recommended or required settings.


Protocol section
----------------

The Protocol section can be used for the following purposes:


  >  Specify the parameters for the TCPIP program.

  >  Specify the parameters for the RFCNBIOS program.

  >  Specify the IPX protocol when running the IPTUNNEL program.


Refer to the Programs section of this guide for samples of each of these uses.


The Protocol section has the following format:

  Protocol protocol_name
     BIND board_name

Usually a protocol binds to the first network board it finds. The BIND
option forces the protocol to bind to the board you specify.

Replace 'board_name' with the name of the board you want the protocol to
bind to. For example, if you want protocol XYZ to bind to your NE2000 board,
your NET.CFG needs the following lines:


Protocol XYZ
  BIND NE2000



Sample configuration files
==========================

The following section provides sample NET.CFG files from the following
configurations:


  >  Ethernet using an NE2000 board with Ethernet_II frame format

  >  Ethernet using an NE2000 board and IPX with 802.3 frame format

  >  Token-Ring using IPX with 802.2 frame format 

  >  ARCnet using a TRXNET board with NOVELL_RX-NET format



Sample NET.CFG file for Ethernet using an NE2000 board
with Ethernet_II frame format:
--------------------------------------------------------




------------------------------------------------------------------------------
Link Support
  Buffers 8 1500
  MemPool 4096

Protocol TCPIP
  ip_address       144.52.6.5
  ip_router        144.52.6.6
  ip_netmask       255.255.252.0

Link Driver NE2000
  Frame Ethernet_II

------------------------------------------------------------------------------








Sample NET.CFG file for Ethernet using an NE2000 board
and IPX with 802.3 format:
------------------------------------------------------



------------------------------------------------------------------------------
Link Support
  Buffers 8 1500
  MemPool 4096

Protocol TCPIP
  ip_address        144.52.6.5
  ip_router         144.52.6.6
  ip_netmask        255.255.252.0

Link Driver NE2000
  Frame Ethernet_II
  Frame Ethernet_802.3
  Protocol IPX 0 Ethernet_802.3

------------------------------------------------------------------------------





Sample NET.CFG file for Token-Ring using IPX with 802.2 format:
---------------------------------------------------------------


------------------------------------------------------------------------------
Link Support
  Buffers 8 1500
  MemPool 4096

Protocol TCPIP
  ip_address        144.52.6.5
  ip_router         144.52.6.6
  ip_netmask        255.255.252.0

Link Driver TOKEN
  Frame TOKEN-RING_SNAP
  Frame TOKEN-RING
  Protocol IPX E0 TOKEN-RING
------------------------------------------------------------------------------




Sample NET.CFG file for ARCnet using a TRXNET board with NOVELL_RX-NET format:
------------------------------------------------------------------------------



------------------------------------------------------------------------------
Link Support
  Buffers 8 1500
  MemPool 4096

Protocol TCPIP
  ip_address      144.52.6.5
  ip_router       144.52.6.6
  ip_netmask      255.255.252.0

Link Driver TRXNET
  Frame NOVELL_RX-NET
------------------------------------------------------------------------------








Sample system files
===================

The next section provides samples of the following system files:


  >  A recommended AUTOEXEC.BAT file

  >  A sample SYSTEM.INI file

  >  A sample LWP.INI file



Recommended 
------------

AUTOEXEC.BAT file: "drive":\AUTOEXEC.BAT:
-----------------------------------------


------------------------------------------------------------------------------
PATH C:\DOS;C:\WINDOWS;C:\XLN\BIN40
SET EXCELAN=C:\XLN
PROMPT $P$G
LSL
NE2000
TCPIP

------------------------------------------------------------------------------



Sample SYSTEM.INI file: "drive":\WINDOWS\SYSTEM.INI:
----------------------------------------------------




------------------------------------------------------------------------------
[boot]
...
[keyboard]
....
[boot.description] 
... 
[386Enh]DEVICE=VTCPIP.386
...
[standard]
....
[NonWindowsApp]
------------------------------------------------------------------------------








Sample LWP.INI file: "drive":\WINDOWS\LWP.INI:
----------------------------------------------




------------------------------------------------------------------------------
[LANWorkPlace]ROOT=C:\XLN; Product root directory
; NOTE: The LAN WorkPlace for DOS programs require many
;       other entries, but the TCP/IP transport only
;       requires the ROOT entry.

------------------------------------------------------------------------------