version		1	u	Protocol version number;
byte_order	1bit	u	Byte order of sender;
auth_msg_type	1	u	Protocol message type and byte order;
name		>=0	a	Athena principal name (user or service);
instance	>=0	a	Athena principal instance (user or service);
realm		>=0	a	Authentication realm name;
group		>=0	a	Athena group name;
time_sec	4	u	timestamp, seconds since midnight Jan 1,1970, in UTC;
time_5ms	1	u	timestamp, 5ms units, add to time_sec, in UTC;
lifetime	1	u	valid ticket lifetime, 5 minute units;
key		8	u	64 bit encryption key;
kvno		1	u	key version number;
n		1	u	count of service entries;
address		4		network host Internet address, IP format;
length		1	u	the length of a field, 0-255, in bytes; 
w_length	2	u	the length of a field, 0-65535, in bytes;
exp_date	4	u	expiration date, seconds since midnight Jan 1,1970, UTC;
direction	1bit	u	within an association,
				zero if sending {addr, port } <
				receiving {addr,port}, else one;
sequence	31bits	u	sequence number, 0...2@+[31]-1 ;
m_id		4	s	message id, direction << 31 + sequence, i.e. 
				direction is sign bit, sequence is magnitude;
app_code	1	u	application specific operation code;
app_data	n		application specific data, arbitrary length;
checksum	4	u	4 byte checksum;
big_checksum	16	u	16byte checksum;
permissions	2	u	The set of permissions for a principal 
				for a given service;
quotas				The set of quotas for a principal for a
				given service;
  quota_1	2	u	1st quota;
  quota_2	2	u	2nd quota;

byte ordering	The least significant bit of @i(auth_msg_type) will
encode the byte ordering for the transmitting host. LSB_FIRST, one,
implies least signigicant byte in lowest address, e.g. Vax and IBM
PCs. MSB_FIRST, zero, implies most significant byte in lowest address,
e.g. Sun 68000.  The transmitter of a message always transmits in
natural host order, and marks its byte ordering in @i(auth_msg_type).
The receiver, if necessary, converts fields to its own byte ordering.

@ux(Protocol Message pattern)

{ version, auth_msg_type, name@-[p], instance@-[p], realm@-[p], time_sec,
 cleartext, ciphertext }

auth_request = 	{ version, auth_msg_type,
	name@-[p], instance@-[p], realm@-[p], time_sec@-[ws], n,
	lifetime@-[1], name@-[s@-[1]], instance@-[s@-[1]], ...
	lifetime@-[n], name@-[s@-[n]], instance@-[s@-[n]] }
	where	auth_msg_type = <AUTH_MSG_KDC_REQUEST>
		n = number of service requests
		and the services requested are local to the realm
		managed by the Kerberos receiving the request

auth_reply = 	{ version, auth_msg_type,
name@-[p], instance@-[p], realm@-[p], time_sec@-[ws], n,
	lifetime@-[1], name@-[s@-[1]], instance@-[s@-[1]], ...
	lifetime@-[n], name@-[s@-[n]], instance@-[s@-[n]],
	kvno@-[p], w_length,
{cipher}K@-[p@-[kvno]] }
	where	auth_msg_type = <AUTH_MSG_KDC_REPLY>
		w_length = length of cipher; zero if @i(name) is unknown;
		cipher =	{ n, length[n],
			K@-[session@-[1]], 
	lifetime@-[service@-[1]], kvno@-[service@-[1]], realm@-[service@-[1]],
	{ticket@-[service@-[1]]}K@-[service@-[1@-[kvno]]], ...
			K@-[session@-[n]], 
	lifetime@-[service@-[n]], kvno@-[service@-[n]], realm@-[service@-[n]],
	{ticket@-[@-[service@-[n]]]}K@-[service@-[n@-[kvno]]],
			time_sec@-[kdc]}

		where length[] = array of lengths of tickets (variable
		size); 
		a length is zero if the service instance is unknown;
	ticket@-[i] = { name@-[p], instance@-[p],
		realm@-[p], address, K@-[session@-[i]],
 		lifetime@-[i], time_sec@-[kdc],
		name@-[s@-[i]], instance@-[s@-[i]] }