## Slide 1: Aircraft Performance
MITFC Ground School
January 13, 2010

## Slide 2: Atmospheric Properties
Aircraft performance charts referenced to ICAO Standard Atmosphere
Standard Pressure
  29.92 in Hg (14.7 psi) at surface
  Decreases 1 in Hg per 1000 ft
Standard Temperature
  15°C at surface
  Decreases 2°C per 1000 ft
Adjustments given for non-standard conditions
Pressure Altitude
Density Altitude

## Slide 3: Pressure Altitude
Altitude in the standard atmosphere that corresponds to the current outside pressure
What the altimeter senses
  Altimeter is corrected to “actual” altitude via altimeter settings, which are broadcasted by airports
Calculated by
  Setting your altimeter to 29.92 “Hg and reading altitude
  Applying a correction factor to the current altitude based on your altimeter setting

## Slide 4: Density Altitude (DA)
Pressure altitude corrected for variations in temperature
Altitude in the standard atmosphere that corresponds to the current outside air density
Density (mass/volume) is affected by altitude, temperature, and humidity
Useful when describing performance
Lower pressure = higher DA
Higher temperature = higher DA
Higher DA = lower aircraft performance
  Reduced lifting medium for wings
  Aircraft stalls at higher speeds
  Engine power is reduced
Stated plainly, higher DA means lower density, or less air molecules to work with

## Slide 5: Altitude Calculation
Find Pressure and Density Altitude
Altimeter setting is 30.12
  On airport at 4200 ft
  (29.92-30.12)*1000 = -200 ft plus 4,200 = 4000 …or….
  Twist altimeter setting to 29.92, and find that the pressure altitude is 4,000 ft
Based on an OAT of 16C, what is Density Altitude?
  5,000 ft

## Slide 6: Aircraft Drag
Parasite Drag
  Produced by aircraft as it moves through air
  Increases with square of airspeed
Induced Drag
  Drag created by lift
  Increases at high Angle of Attack/Lower Airspeed

## Slide 7: Engine Performance
Common types
  IC (internal combusion)
    Most GA Aircraft
    Cars
  Turboprop
  Turbofans
Power decreases with density altitude
Thrust decreases with airspeed (propellers)
Variable pitch propellers (constant speed prop) offer better propeller efficiency over wider range
Basic GA aircraft use fixed-pitch props

## Slide 8: Steady Level Flight
Power = Thrust * Velocity
  = Drag * Velocity in steady flight
For propeller aircraft, at a given throttle setting, power approximately constant with speed
  Less thrust at higher speeds

## Slide 9: Cruise Flight

## Slide 10: Climbing Flight
Use of excess power to push plane upwards
Excess power drives climb rate
Excess thrust drives climb angle

## Slide 11: Climb Performance

## Slide 12: Takeoff Performance
Runway Conditions: Bad
  Wet runways
  Grass
  Dirt
Effects of Wind
  Headwind = reduced takeoff distance
  Tailwind = increased takeoff distance
Crosswind
  Component of wind in direction perpendicular to aircraft direction
  Aircraft have crosswind limits

## Slide 13: Takeoff Performance

## Slide 14: V-Speeds
TAS – True Airspeed
IAS – Indicated Airspeed
V_s1 – Stall speed in standard configuration
V_x - Best Angle of Climb Airspeed
V_y – Best Rate of Climb Airspeed
V_a – Maneuvering speed (max deflection of controls safe)
V_ne – Never Exceed Airspeed