## Slide 1: Basic Airplane Instruments
Jason Maloney
MITFC Ground School
Fall 2009

## Slide 2: Pitot-Static System & Instruments
Airspeed Indicator (Pitot and Static)
Vertical Speed Indicator (Static)
Altimeter (Static)
Pitot Heat to prevent/melt ice

## Slide 3: Altimeter
Wafers sealed at Standard Pressure of 29.92” Hg
Adjust altimeter setting in Kollsman Window
  1”Hg = 1,000 ft
  Set to field elevation if no setting available
Types of Altitude:
  Indicated Altitude
  True Altitude (MSL)
  Pressure Altitude
  Absolute Altitude (AGL)
  Density Altitude

## Slide 4: Nonstandard Temp. & Pressure
“High to Low or Hot to Cold, look out below!”

## Slide 5: Vertical Speed Indicator (VSI)
Rate of climb or descent in feet per minute
Static pressure differential instrument
Wafers at ambient pressure
Diaphragm exposed to ambient pressure, but with calibrated leak
VSI lags
Trend and Rate information

## Slide 6: Airspeed Indicator (ASI)
Dynamic and static pressure differential
Types of Airspeed:
  Indicated (IAS)
  Calibrated (CAS)
  True (TAS)
  Groundspeed (GS)
Some V-speeds
  Vso -stall w/ flaps (“dirty”)
  Vs1-stall w/o flaps (“clean”)
  Vfe -max flap extend
  Vno -max structural cruise
  Vne -never exceed

## Slide 7: Blocked Pitot Tube (inlet only)
Ram air exits via drain
Pressure equalizes to static
ASI decreases to zero

## Slide 8: Blocked Pitot System (inlet and drain)
ASI Frozen at constant altitude
ASI acts as an altimeter:
  A climb will show an increased airspeed
  Descent will show decreased airspeed
Potentially very dangerous!!
  Why?
  What should happen as you climb? Descend?
  Can lead to stall and/or in-flight breakup

## Slide 9: Blocked Static Port
ASI continues to operate, but incorrectly
  Behaves somewhat as an altimeter
VSI reads zero
Altimeter frozen at altitude where blockage occurred
Try alternate static source
  Mechanical, or
  Break face of VSI

## Slide 10: Gyroscopes & Precession
Rigidity in Space
Precession
  Force felt 90° later in direction of rotation
Air flow from vacuum system

## Slide 11: Vacuum System and Instruments
Monitor vacuum pressure during flight
Some airplanes have back-up vacuum source

## Slide 12: Turn & Slip / Turn Coordinator
Principle of Precession
Turn coordinator shows both rate of roll and rate of turn (canted gyro)
Turn-and-slip only shows rate of turn

## Slide 13: Turn Coordination
“Step on the ball”
Coordinated turns will help prevent spins
Standard rate turn
  3° per second
  2 minute turn

## Slide 14: Attitude Indicator (ADI)
Principle of Rigidity in Space
Instantaneous indications
Your aircraft rotates around the gyro

## Slide 15: Reading an Attitude Indicator
Compare miniature airplane to artificial horizon
Adjust airplane to match horizon during straight-and-level flight

## Slide 16: Directional Gyro (DG) a.k.a. Heading Indicator
Principle of Rigidity in Space
Must set the DG to a known heading before use
Readjust periodically due to precession

## Slide 17: Magnetic Compass & Errors
Variation
  Magnetic vs. True North
  Reference Isogonic lines
Dip: Northern Hemisphere Turning Error
  Undershoot North, Overshoot South (UNOS)
  Accurate indication at 90 & 270
Dip: Acceleration Error
  On East or West heading:
  Accelerate North, Decelerate South (ANDS)
Deviation
  Local magnetic fields (i.e. from radio)