## Slide 1: Stability and Flight Controls

## Slide 2: Three Axes of Flight
Longitudinal (green)
  Nose to tail
Lateral (blue)
  Wing tip to Wing tip
Vertical (red)
  Top to bottom
Glenn Fisher Private Pilot Ground School
Arm
Moment
Force

## Slide 3: Controls

## Slide 4: The Flight Controls
Pitch
  Motion about the lateral axis
  Controlled by the elevator
Roll
  Motion about the longitudinal axis
  Controlled by the ailerons
Yaw
  Motion about the vertical axis
  Controlled by the rudder
Glenn Fisher Private Pilot Ground School

## Slide 5: Adverse Yaw (or why we have a Rudder)
Induced drag
  increase in lift = increase in drag
If we want to roll to left
  Yoke turns to left
  Left aileron goes up, right aileron goes down
  Right wing develops more lift, therefore more drag
  And Plane tries to yaw in opposite direction to roll
Glenn Fisher Private Pilot Ground School

## Slide 6: Static Stability
Positive (stable)
  Ball returns to starting position when disturbed
Neutral
  Ball remains in new position when disturbed
Negative (unstable)
  Ball moves away from starting position when disturbed
Glenn Fisher Private Pilot Ground School

## Slide 7: Static Stability (continued)
Glenn Fisher Private Pilot Ground School

## Slide 8: Dynamic Stability
Positive
  Oscillations decrease in amplitude with time
Neutral
  Oscillations are constant in amplitude with time
Negative
  Oscillations increase in amplitude with time
Above are all types of Positive Static Stability
Link to animation of dynamic longitudinal stability
Glenn Fisher Private Pilot Ground School

## Slide 9: Longitudinal Stability
Stability about lateral axis
AKA Pitch Stability
Dependent on location of Center of Gravity
  CG too far forward
    Stable (too stable)
  CG too far aft
    Unstable
    Stall Recovery Difficult
    JAS 39 Gripen Crash 1
    JAS 39 Gripen Crash 2
Glenn Fisher Private Pilot Ground School
Pitch up moment
Pitch down moment
Angle of attack
Stable
Unstable

## Slide 10: Lateral Stability
Stability about longitudinal axis
AKA Roll Stability
Can be influenced by
  Dihedral
  Sweepback
  High vs. Low Wing
Glenn Fisher Private Pilot Ground School

## Slide 11: Increasing Lateral Stability
Dihedral
Wing Placement

## Slide 12: Directional Stability
Stability about vertical axis
Influenced by size and location of vertical stabilizer
  Similar to weather vane or feathers on an arrow
Glenn Fisher Private Pilot Ground School

## Slide 13: Stall
At certain angle of attack airflow cannot “stick” to top of wing
Air flow separation occurs
Glenn Fisher Private Pilot Ground School

## Slide 14: Stall
The “critical angle of attack” does not change for a given wing
Large loss of lift when stalled
Stall Video
F-22 Stall Video
Glenn Fisher Private Pilot Ground School

## Slide 15: Spins
Uncoordinated stalls result in spins
Both wings are stalled, 1 wing “more” stalled than other
Rotating helical downward path
Easy to recover from in Cessna 172
You won’t have to do this during training
Video 1
Video 2
Video 3
Glenn Fisher Private Pilot Ground School

## Slide 16: Aerodynamics of Maneuvering Flight

## Slide 17: Climbing Flight
Airplane climbs due to inclined thrust vector
4 Forces are still in equilibrium
Rate at which airplane climbs determined by excess thrust
Glenn Fisher Private Pilot Ground School

## Slide 18: Left Turning Tendencies
Torque
P Factor
Spiraling Slip Stream
Gyroscopic Precession
  This is not always a left turning tendency
Glenn Fisher Private Pilot Ground School

## Slide 19: Descending Flight
Airplane descends when flight path is pointed downward
4 Forces are still in equilibrium
Glenn Fisher Private Pilot Ground School

## Slide 20: Turning Flight
Horizontal component of lift turns plane
Rudder is used to maintain coordination
4 forces are not in equilibrium, this is accelerated flight
Glenn Fisher Private Pilot Ground School

## Slide 21: Load Factor
Ratio of weight supported by wings to weight of aircraft
AKA as G’s
A load factor of 2, or 2 G’s means wings support twice aircraft weight
Increasing load factor increases stall speed
Glenn Fisher Private Pilot Ground School