## Slide 1
MITFC Ground School Fall 2009
Jason Maloney

## Slide 2
Sump fuel during preflight
Fill tanks after flight to avoid condensation

## Slide 3
Fuel/Air Mixture:
  Rich – High Fuel/Air ratio
  Lean – Low Fuel/Air ratio
Lean the mixture during climb
Enrich the mixture during descent
High Density Altitude = Low Air Density  lean the mixture

## Slide 4
Indications
  RPM decrease
  Engine Roughness
Carb. Heat Enriches Mixture
Use Carb. Heat at low power settings
If Carb. Ice present, carb. heat will lead to RPM decrease, then RPM increase as ice melts
Notes: <number>

## Slide 5
Reciprocating Engine
Four Strokes
  Intake
  Compression
  Power
  Exhaust

## Slide 6
Detonation
  Explosive Combustion
  Occurs when mixture too lean or fuel grade too low
  If detonation is suspected, try enriching the mixture or increasing airspeed
Pre-ignition
  caused by hot spots in cylinder and/or cylinder damage

## Slide 7
Magnetos provide self sufficient spark to cylinders
Mag. Check during runup
Engine will run with electrical system off
Two spark plugs per cylinder

## Slide 8
Functions:
  Lubrication of the engine’s moving parts
  Cooling of the engine by reducing friction
  Removing heat from the cylinders
  Providing a seal between the cylinder walls and pistons
  Carrying away contaminants
Always check oil pressure immediately after starting engine
Monitor oil temperature/pressure during flight

## Slide 9
Fixed Pitch:
  Throttle controls RPM
Constant Speed:
  Throttle controls power output (manifold pressure)
  Propeller control regulates engine RPM  in turn regulates propeller RPM via automatic pitch changes
Notes: <number>

## Slide 10
Tricycle landing gear
Tail wheel / Conventional
  Pilot must log ground instruction and receive endorsement from CFI

## Slide 11
Non-flashing
Position Lights required for Night Flight